## Slide 1: GPS Status and Modernization
Maj Wesley Chidester
Deputy Chief, Systems Engineering & Integration
GPS Wing, Air Force Space Command
GEOSpatial Information Systems for Transportation Symposium
Charleston, WV
12-14 April 2010
"This briefing is for information only. No US Government commitment to
sell, loan, lease, co-develop or co-produce defense articles or provide
defense services is implied or intended."
"DISTRIBUTION A: Approved for public
release; distribution unlimited"

## Slide 2: Overview
GPS Overview
Recent Events
Modernization Improvements

## Slide 3: Critical Asset
Available, reliable, accurate, and free of charge
Vital to International Security, Economic Growth, and Public Safety
    Creates an irreplaceable advantage for warfighters and civil communities
Extends across all domains -- air, land, sea, space, cyberspace
Effects transcend national and military boundaries
    Simultaneously creates strategic and tactical, global and local effects

## Slide 4
Very robust constellation
  30 space vehicles currently in operation
    11 GPS IIA
    12 GPS IIR
    7 GPS IIR-M
  4 additional satellites in residual status
  1 additional IIR-M waiting to be set healthy
Global GPS civil service performance commitment met continuously since December 1993
Next Launch – IIF-1, May 2010
GPS – Serving the World

## Slide 5: GPS Ground Segment
Operated by Space Professionals in 2d Space Operations Squadron at Schriever AFB, CO
Backup facility at Vandenberg AFB, CA
Global network of 16 ground monitoring sites and 12 ground antennas
Hawaii
Cape Canaveral
Ascension
Diego Garcia
Kwajalein
Schriever AFB
Vandenberg
AFB
USNO Wash, DC
England
Bahrain
Ecuador
Argentina
South Africa
Tahiti
Alaska
Australia
New Zealand
South Korea

## Slide 6
System accuracy exceeds published standard
SPS Signal in Space Performance
(Root Mean Square (RMS) over all SPS SIS URE)
2001 SPS Performance Standard
(RMS over all SPS SIS URE)
2008 SPS Performance Standard
Selective Availability
RMS Signal-in-Space User Range Error (URE), meters
N/A
N/A
N/A
N/A
N/A

## Slide 7: GPS Modernization Programs
GPS II R / IIR-M
2005
IIA/IIR capabilities plus
2nd civil signal (L2C)
M-Code (L1M & L2M)
GPS IIA
1995
Standard Service
  Single frequency (L1)
  Coarse acquisition code navigation
Precise Service
  Y-Code (L1Y & L2Y)
GPS IIF
2010
IIR-M capability plus
3rd civil signal (L5)
12 year design life
GPS III
2014 - 2025
Backward compatible
4th civil signal (L1C)
Increased availability
Increased integrity
Ground Control Segment
Architecture Evolution Plan
(AEP)
Next Generation
Control Segment
(OCX)
Legacy
Control
System
Space
Segment

## Slide 8: GPS Modernization – Ground
Architecture Evolution Plan (AEP)
  Transitioned in 2007
  Modern distributed system replaced 1970’s mainframes
  Increased capacity for monitoring of GPS signals to 100% worldwide coverage (was 96.4%) and have 99.8% of world double covered
  Increased worldwide commanding capability from 92.7% to 94.5% while providing nearly double the backup capability
Next Generation Operational Control Segment (OCX)
  Enables modernized messaging
  Controls more capable GPS constellation
  Monitors all GPS signals
  $1.53B contract awarded 25 February 2010

## Slide 9: GPS Modernization – New Civil Signals
Second civil signal “L2C”
  Designed to meet commercial needs
  Higher accuracy through ionospheric correction
  1st launch: Sep 2005 (GPS IIR-M); 24 satellites: ~2016
Third civil signal “L5”
  Designed to meet demanding requirements for transportation safety-of-life
  1st launch: ~ 2010 (GPS IIF); 24 satellites: ~2018
Fourth civil signal “L1C”
  Designed with international partners for GNSS interoperability
  Begins with GPS Block III
  1st launch: ~2014; 24 satellites: ~2021

## Slide 10: GPS Expandable
Optimize GPS assets to improve operational effectiveness for global users & terrain challenged environments
  Increase the number of vehicles over head for better availability/coverage
  Constellation expansion feasible with robust number of satellites now on-orbit
Consistent with the current Standard Positioning Service (SPS) Performance Standard
  Adjust position of satellites in 3 of 6 orbital planes to create expanded constellation
  Expanded constellation provides better GLOBAL coverage
Current Operations
Expanded Operations

## Slide 11: Keys to the Global Success of GPS
Program Stability and Performance
  Civil service performance commitment met continuously since 1993
  Continuous improvements in accuracy, availability, etc.
  Continuity of constellation and signals ensured through Air Force operation and acquisition
  Funding through U.S. taxpayers
Policy Stability and Transparency
  Open access to civil GPS signals, free of direct user fees
  Open, free, and stable technical documentation
  Market-based competition worldwide
  National-level policy coordination including civil and military leaders
Commercial Entrepreneurship and Investment
Continuous Modernization thru Technology Investment

## Slide 12: Summary
Largest constellation in history with best accuracy ever
Modernized Command and Control System allows more signal monitoring and quicker satellite commanding than ever before
Constant improvements through constellation management
And we’re continuing to modernize and improve GPS even more!
GPS -- Serving the World

## Slide 13: GPS Status and Modernization
GEOSpatial Information Systems for Transportation Symposium
Charleston, WV
12-14 April 2010
Maj Wesley Chidester
Deputy Chief, Systems Engineering & Integration
GPS Wing, Air Force Space Command
"DISTRIBUTION A: Approved for public
release; distribution unlimited"
"This briefing is for information only. No US Government commitment to
sell, loan, lease, co-develop or co-produce defense articles or provide
defense services is implied or intended."