## Slide 1: GPS and Worldwide GNSS Interoperability
Workshop on the Applications of GNSS
Chisinau, Moldova
17-21 May 2010
Jeffrey Auerbach
Advisor on GNSS Affairs
Office of Space and Advanced Technology
U.S. Department of State
Notes: 03/12/08
<number>

## Slide 2: Overview
U.S. Space-Based PNT Policy
GPS & U.S. Augmentation Programs Status
International Cooperation Activities
<number>

## Slide 3: U.S. Space-Based PNT Policy
Provide uninterrupted availability of PNT services
Meet growing national, homeland, economic security, and civil requirements, and scientific and commercial demands
Remain the pre-eminent military space-based PNT service
Continue to provide civil services that exceed or are competitive with foreign civil space-based PNT services and augmentation systems
Remain essential components of internationally accepted PNT services
Promote U.S. technological leadership in applications involving space-based PNT services
GOAL: Ensure the U.S. maintains space-based PNT services, augmentation, back-up, and service denial capabilities that…
<number>
Notes: <number>

## Slide 4: U.S. Policy Promotes Global Use of GPS Technology
No direct user fees for civil GPS services
  Provided on a continuous, worldwide basis
Open, public signal structures for all civil services
  Promotes equal access for user equipment manufacturing, applications development, and value-added services
  Encourages open, market-driven competition
Global compatibility and interoperability with GPS
Service improvements for civil, commercial, and scientific users worldwide
Protection of radionavigation spectrum from disruption and interference
<number>

## Slide 5: Overview
U.S. Space-Based PNT Policy
GPS & U.S. Augmentation Programs Status
International Cooperation Activities
<number>

## Slide 6: GPS Constellation Status
11 Block IIA
12 Block IIR
7 Block IIR-M
  Transmitting new second civil signal
  1 GPS IIR-M in on-orbit testing
3 additional satellites in residual status
  Next launch: IIF scheduled 21 May 2010
Global GPS civil service performance commitment met continuously since December 1993
30 Operational Satellites (Baseline Constellation: 24)
<number>

## Slide 7: GPS Modernization Program
Block IIA/IIR
Block III
Block IIR-M, IIF
Backward compatibility
4th civil signal (L1C)
Increased accuracy
Increased anti-jam power
Assured availability
Navigation surety
Controlled integrity
Increased security
System survivability
IIR-M: IIA/IIR capabilities plus
2nd civil signal (L2C)
M-Code (L1M & L2M)
IIF: IIR-M capability plus
3rd civil signal (L5)
Anti-jam flex power
Basic GPS
Standard Service
  Single frequency (L1)
  Coarse acquisition (C/A) code navigation
Precise Service
  Y-Code (L1Y & L2Y)
  Y-Code navigation
Increasing System Capabilities  Increasing Defense / Civil Benefit
<number>
Notes: <number>
Incremental “Block” strategy for both space and ground
  Solid system engineering foundation & processes
  Mission assurance framework
  Stable requirements (approved CDD)
  Capability Insertion effort focused to deliver IIIC needs
  Regular independent reviews of performance and adherence to engineering process
Synchronized capability between space and ground segments
OCX Block I will provide backwards compatibility to the legacy system

## Slide 8: SPS Signal in Space Performance
System accuracy exceeds published standard
<number>

## Slide 9: FAA GPS Augmentation Programs
<number>
Notes: <number>

## Slide 10: Wide Area Augmentation System (WAAS) Architecture
38 Reference
Stations
3 Master
Stations
4 Ground
Earth Stations
Geostationary
Satellite Links
2 Operational
Control Centers
4F3
98 W
<number>
Notes: <number>
The Wide Area Augmentation System (WAAS) is one of 4 Space Based Augmentation Systems (SBAS) in operation or in development around the globe. The Japanese MSAS, and Indian GAGAN systems are similar to the U.S. WAAS, and the EU has the EGNOS system.
The WAAS configuration consists of 38 Wide Area Reference Stations (WRS) feeding data to 3 Wide Area Master Stations (WMS), that compute GPS corrections and integrity information which is forwarded to four geographically dispersed Ground Earth Stations (GES), and uplinked as messages to two geostationary earth orbiting (GEO) satellites and broadcast to the users. The system is controlled from two Operational Control Centers (OCC), one located at the National Operational Command Center (NOCC) in Herndon, VA and the second located at the Pacific Operational Control Center (POCC) in San Diego, CA. A third GEO is being added to meet availability and continuty requirements.

## Slide 11: WAAS LPV Coverage
<number>
Note: Display does not account for Intelsat Galaxy 15 satellite anomaly

## Slide 12: Local Area Augmentation System (LAAS)
Architecture
  Ground Station/Processing Unit/Power Supply (one shelter on airport property)
  4 Reference Receivers/Antennas
  VHF Data Link Antenna
Specifications
  Supports Category I approach with growth to Category III
  Single facility can provide service up to 23 mile radius
<number>
Notes: <number>
LAAS system consists of LAAS ground station/processing unit/power supply (one shelter on airport property), 4 reference receivers/antennas, one VHF data link antenna. LAAS uses a similar approach to WAAS except all of the equipment is installed at the airport and the corrections and integrity information is transmitted to the aircraft via a local VHF transmitter. LAAS accuracy is typically 2-3 times better than WAAS and the system is designed to support landing operations is zero visibility conditions, commonly referred to at Category-III operations. LAAS provides a more cost beneficial alternative to legacy landing systems because a single facility can provide service to all runways at an airport and the precise positioning service is available 360 degrees coverage out to 23 miles to enable three dimensional arrivals, closely space parallel runway operations, and NextGen super density operations.

## Slide 13: LAAS/GBAS International Efforts
Agana, Guam
Frankfurt, Germany
Rio De Janeiro, Brazil
Malaga, Spain
Sydney, Australia
Bremen, Germany
<number>
Notes: <number>
There are several Category-I LAAS prototypes installed at locations around the world. The Category-I system design approval at Memphis is expected to facilitate similar approvals for LAAS systems in Australia, Germany, and Spain. The SDA approval at Memphis was achieved as a result of international cooperation between Airservices Australia, and the FAA.

## Slide 14: Nationwide Differential GPS (NDGPS) is a National PNT Utility
Operated/managed by U.S. Coast Guard as a Combined NDGPS (Maritime + Department of Transportation sites + ACOE sites)
System Specifications
  Corrections broadcast at 285 and 325 kHz using Minimum Shift Keying (MSK) modulation
  Real-time differential GPS corrections provided in Radio Technical Commission for Maritime Services (RTCM) SC-104 format
  No data encryption
  Real-time differential corrections for mobile and static applications
Single coverage terrestrial over 92% of Continental United States (CONUS) ; double coverage over 65% of CONUS
<number>
Notes: <number>

## Slide 15: Nationwide Differential GPS
Expansion of maritime differential GPS (DGPS) network to cover terrestrial United States
Built to international standard adopted in 50+ countries
<number>

## Slide 16: Terrestrial NDGPS Capabilities and Uses
Transportation operational requirements:
  Federal Highway Administration (FHWA)
      on behalf of state and local DOT stakeholders
      routine use in Federal-Aid Program
      survey, construction, quality, asset management
      roadside management
      law enforcement
  Association of Am. Railroads
      baseline reference
  National Governor’s Association
      use by state DOTs
      resource management
      agencies
<number>
Notes: <number>

## Slide 17: National Continuously Operating Reference Stations (CORS)
Enables highly accurate, 3-D positioning
  Centimeter-level accuracy
  Tied to National Spatial Reference System
1,300+ sites operated by 200+ public, private, academic organizations
NOAA’s Online Positioning User Service (OPUS) automatically processes coordinates submitted via the web from around the world
OPUS-RS (Rapid Static) declared operational in 2007
NOAA considering support for real-time networks
<number>
Notes: <number>

## Slide 18: Overview
U.S. Space-Based PNT Policy
GPS & U.S. Augmentation Programs Status
International Cooperation Activities
<number>

## Slide 19: Planned GNSS
Global Constellations
  GPS (24+)
  GLONASS (30)
  Galileo (27+3)
  Compass (30 + 5 GEO)
  GINS - Global Indian Navigation System (24)
Regional Constellations
  QZSS (3)
  IRNSS (7)
Satellite-Based Augmentations
  WAAS (2+1)
  MSAS (2)
  EGNOS (3)
  GAGAN (2)
  SDCM (2)
<number>
Notes: 03/12/08
<number>

## Slide 20: Current International Signal Plans
Future
CDMA signal
SBAS
(US, Europe India, Japan)
QZSS
(Japan)
IRNSS/GINS
(India)
COMPASS
(China)
Galileo
(Europe)
GLONASS
(Russia)
GPS
(US)
L1
L5
L2
Compass & IRNSS
In S-band
Note: GINS modulations TBD
<number>
Notes: <number>

## Slide 21: U.S. Objectives in Working with Other GNSS Service Providers
Ensure compatibility ― ability of U.S. and non-U.S. space-based PNT services to be used separately or together without interfering with each individual service or signal
  Radio frequency compatibility
  Spectral separation between M-code and other signals
Achieve interoperability – ability of civil U.S. and non-U.S. space-based PNT services to be used together to provide the user better capabilities than would be achieved by relying solely on one service or signal
  Primary focus on the common L1C and L5 signals
Ensure a level playing field in the global marketplace
Pursue through Bi-lateral and
Multi-lateral Cooperation
<number>
Notes: 03/12/08
<number>

## Slide 22: U.S. - Europe Cooperation
2004 U.S.-EU agreement provides foundation for cooperation
Four working groups were set up under the agreement:
  Technical, trade, next generation systems and security working groups
Improved new civil signal (MBOC) adopted in July 2007
Technical working group meetings, May 2010 in Brussels
Oct. 22, 2008 , EU-U.S. Plenary delegations meeting under the auspices of the GPS-Galileo Cooperation Agreement
Signing ceremony for GPS-Galileo Cooperation Joint Statement, Oct. 23, 2008
(Michel Bosco, European Commission;
Kenneth Hodgkins, U.S. Department of State)
<number>
Notes: 03/12/08
<number>

## Slide 23: Additional Bilateral Cooperation
<number>
U.S.-Japan Joint Statement on GPS Cooperation in 1998
  Japan’s Quasi Zenith Satellite System (QZSS) designed to be fully compatible and highly interoperable with GPS
  Bilateral agreements to set up QZSS monitoring stations in Hawaii and Guam. Guam station completed!
U.S.-Russia Joint Statement issued in Dec. 2004
  Negotiations for a U.S.-Russia Agreement on satellite navigation cooperation underway since late 2005
  Working Groups on compatibility/interoperability, search and rescue
U.S.-India Joint Statement on GNSS Coop. in 2007
  Technical Meetings focused on GPS-India Regional Navigation Satellite System (IRNSS) compatibility and interoperability held in 2008 and 2009
<number>
Notes: 03/12/08
<number>

## Slide 24: International Committee on Global Navigation Satellite Systems (ICG)
  U.S. strongly supports ICG activities
    U.S. hosted ICG-3 at Pasadena, California in 2008
    U.S. contributes to UNOOSA to support ICG meetings and activities
  U.S. pleased with progress made at ICG-4 at St. Petersburg, Russia
    Adoption of new principle on transparency for open services: Every provider should publish documentation that describes signal and system information, policies of provision and minimum levels of performance for its open services
  ICG-5 to be held in October 2010 in Turin, Italy
<number>
Notes: <number>

## Slide 25: Summary
GPS performance is better than ever and will continue to improve
  Augmentations enable even higher performance
  New civil GPS signal available now
  Many additional upgrades scheduled
U.S. policy encourages worldwide use of civil GPS and augmentations
International cooperation is a priority
  Compatibility and interoperability very important
<number>

## Slide 26: Contact Information
Jeffrey Auerbach
Advisor on GNSS Affairs
Office of Space and Advanced Technology
U.S. Department of State
OES/SAT, SA-23, Suite 410
Washington, D.C. 20520
+1.202.663.2388 (office)‏
auerbachjm@state.gov
http://www.state.gov/g/oes/sat/
http://pnt.gov/international/
<number>