## Slide 1: Aviation Benefits of GNSS Augmentation
Workshop on "GNSS Applications for Human Benefit and Development“
Prague, Czech Republic
24-25 September 2010
Jeffrey Auerbach
Advisor on GNSS Affairs
Office of Space and Advanced Technology
U.S. Department of State
Notes: 03/12/08
<number>

## Slide 2: Overview
GBAS/LAAS Capabilities and the Future
Benefits of SBAS/WAAS
Global SBAS and Aviation – Where are We Headed?
<number>
Notes: 03/12/08
<number>

## Slide 3: U.S. GPS Augmentation Programs Designed for Aviation
<number>
Notes: <number>

## Slide 4: Local Area Augmentation System (LAAS)
Aviation Capabilities
Precision approach for ILS Category - I, II, III approaches
Multiple runway coverage at an airport
3D RNP procedures (can be supported by multiple navigation sources)
Continuous Decent Arrivals (CDA)
Navigation for closely spaced parallel runways
Ground Based Augmentation System (GBAS)
Designed for aviation use
<number>
Notes: <number>
LAAS system consists of LAAS ground station/processing unit/power supply (one shelter on airport property), 4 reference receivers/antennas, one VHF data link antenna. LAAS uses a similar approach to WAAS except all of the equipment is installed at the airport and the corrections and integrity information is transmitted to the aircraft via a local VHF transmitter. LAAS accuracy is typically 2-3 times better than WAAS and the system is designed to support landing operations is zero visibility conditions, commonly referred to at Category-III operations. LAAS provides a more cost beneficial alternative to legacy landing systems because a single facility can provide service to all runways at an airport and the precise positioning service is available 360 degrees coverage out to 23 miles to enable three dimensional arrivals, closely space parallel runway operations, and NextGen super density operations.

## Slide 5: LAAS Next Steps
Category-I system design approval at Memphis – Complete
Category-III ICAO technical validation completed (May 2010)
Category-III final investment decision by - 2012
<number>
Notes: <number>
The FAA approved the Honeywell Category-I LAAS on September 4th, 2009. Based on the lessons learned from the Category-I experience, the FAA will develop a Category-III LAAS prototype, followed by an investment decision for procurement of Category-III systems by 2012. Will not be amended SARPS in 2010.

## Slide 6: GBAS/LAAS Usage
Current airlines GBAS equipped
  Continental, Delta Airlines, Qantas, Air Berlin, TuiFly, Sonair, Air Vanatu, Emirates
More than 15 countries have active GBAS programs
<number>
Installed
Planned
S-CAT I
Notes: <number>
The FAA approved the Honeywell Category-I LAAS on September 4th, 2009. Based on the lessons learned from the Category-I experience, the FAA will develop a Category-III LAAS prototype, followed by an investment decision for procurement of Category-III systems by 2012. Will not be amended SARPS in 2010.

## Slide 7: Wide Area Augmentation System (WAAS)
Satellite Based Augmentation System (SBAS)
Designed for aviation use, but available and used by many GPS users today
Localizer Performance with Vertical Guidance (LPV)-200 approach is comparable to ILS Category I
<number>
Notes: <number>
LAAS system consists of LAAS ground station/processing unit/power supply (one shelter on airport property), 4 reference receivers/antennas, one VHF data link antenna. LAAS uses a similar approach to WAAS except all of the equipment is installed at the airport and the corrections and integrity information is transmitted to the aircraft via a local VHF transmitter. LAAS accuracy is typically 2-3 times better than WAAS and the system is designed to support landing operations is zero visibility conditions, commonly referred to at Category-III operations. LAAS provides a more cost beneficial alternative to legacy landing systems because a single facility can provide service to all runways at an airport and the precise positioning service is available 360 degrees coverage out to 23 miles to enable three dimensional arrivals, closely space parallel runway operations, and NextGen super density operations.

## Slide 8: WAAS Architecture
<number>
38 Reference
Stations
3 Master
Stations
4 Ground
Earth Stations
2 Geostationary
Satellite Links
2 Operational
Control Centers
Notes: <number>
LAAS system consists of LAAS ground station/processing unit/power supply (one shelter on airport property), 4 reference receivers/antennas, one VHF data link antenna. LAAS uses a similar approach to WAAS except all of the equipment is installed at the airport and the corrections and integrity information is transmitted to the aircraft via a local VHF transmitter. LAAS accuracy is typically 2-3 times better than WAAS and the system is designed to support landing operations is zero visibility conditions, commonly referred to at Category-III operations. LAAS provides a more cost beneficial alternative to legacy landing systems because a single facility can provide service to all runways at an airport and the precise positioning service is available 360 degrees coverage out to 23 miles to enable three dimensional arrivals, closely space parallel runway operations, and NextGen super density operations.

## Slide 9: GPS WAAS/SBAS Aviation Benefits
Increased Runway Access
More direct en route flight paths
New precision approach services
Reduced and simplified equipment on board aircraft
Potential elimination of some ground-based navigation aids (NDB, VOR, ILS) can provide a cost saving to air navigation service provider
<number>
Notes: <number>
LAAS system consists of LAAS ground station/processing unit/power supply (one shelter on airport property), 4 reference receivers/antennas, one VHF data link antenna. LAAS uses a similar approach to WAAS except all of the equipment is installed at the airport and the corrections and integrity information is transmitted to the aircraft via a local VHF transmitter. LAAS accuracy is typically 2-3 times better than WAAS and the system is designed to support landing operations is zero visibility conditions, commonly referred to at Category-III operations. LAAS provides a more cost beneficial alternative to legacy landing systems because a single facility can provide service to all runways at an airport and the precise positioning service is available 360 degrees coverage out to 23 miles to enable three dimensional arrivals, closely space parallel runway operations, and NextGen super density operations.

## Slide 10: WAAS Approach Procedures Today
<number>
2209 LPV Approaches as of 26 August 2010 Publication
Notes: <number>

## Slide 11: SBAS Future Considerations
Dual frequency GNSS services in protected aeronautical bands
  Enables aircraft receiver direct estimation and removal of ionospheric delay errors
    Single largest source of vertical position uncertainty
Most significant remaining threats are satellite failure based
  Design a new VPL equation targeting single satellite faults
India, Russia (and potentially China) are developing SBAS systems
Investigate potential to expand LPV to global coverage
<number>
Notes: <number>

## Slide 12: Current SBAS Reference Networks
<number>
Notes: <number>

## Slide 13: Current LPV-200 Coverage (Single Frequency GPS)
WAAS
EGNOS
MSAS
<number>
Modeling provided by Stanford University
Note: Model does not account for Intelsat Galaxy 15 satellite anomaly
Notes: <number>

## Slide 14: Future LPV-200 Coverage (Dual Frequency GPS)
WAAS
EGNOS
MSAS
<number>
Modeling provided by Stanford University
Notes: <number>

## Slide 15: Current + Future Planned Reference Networks
<number>
Notes: <number>

## Slide 16: Future LPV-200 Coverage (Dual Frequency GPS + Additional SBAS)
WAAS
EGNOS
MSAS
GAGAN
SDCM
<number>
Modeling provided by Stanford University
Notes: <number>

## Slide 17: Current + Future Planned + Expanded Reference Networks
<number>
Notes: <number>

## Slide 18: Future LPV-200 Coverage (Dual Frequency GPS + Additional SBAS and Expanded Networks)
WAAS
EGNOS
MSAS
GAGAN
SDCM
<number>
Modeling provided by Stanford University
Notes: <number>

## Slide 19: Future LPV-200 Coverage (Dual Frequency GPS + Expanded Networks + Two GNSS Constellations)
WAAS
EGNOS
MSAS
GAGAN
SDCM
<number>
Modeling provided by Stanford University
Notes: <number>

## Slide 20: Summary
GBAS/LAAS making progress toward ultimate goal of providing Category III capability
Single frequency coverage is good within the countries fielding SBAS
Dual frequency extends LPV coverage outside reference networks
Expanding networks into southern hemisphere could allow global coverage of land masses
Multi-Constellation SBAS allows even greater coverage with fewer stations
  Compatible Geodesy and Time Standards are Important
<number>

## Slide 21: Contact Information
<number>
Jeffrey Auerbach
Advisor on GNSS Affairs
Office of Space and Advanced Technology
U.S. Department of State
OES/SAT, SA-23, Suite 410
Washington, D.C. 20520
+1.202.663.2388 (office)‏
auerbachjm@state.gov
http://www.state.gov/g/oes/sat/
http://gps.faa.gov/
http://pnt.gov/
Notes: 03/12/08
<number>