## Slide 1: GPS Augmentations and Applications
Workshop on the Applications of Global Navigation Satellite Systems
Dubai, United Arab Emirates
16-20 January 2011
Jeffrey Auerbach
GNSS Policy Advisor
Office of Space and Advanced Technology
U.S. Department of State
Notes: 03/12/08
<number>

## Slide 2: Overview
GPS Interface Specifications & Performance Standards
U.S. Augmentations to GPS
  NDGPS
  CORS
  GDGPS & TASS
  GBAS
  SBAS/WAAS
Increased Accuracy with Augmentation
<number>
Notes: <number>

## Slide 3: Public Interface Specifications
Current versions of the public GPS Signal-in-Space (SIS) Interface Specifications:
  IS-GPS-200 – L1 (P(Y) , C/A), L2 (P(Y), L2C)
  IS-GPS-705 – L5
  IS-GPS-800 – L1C
These and other key IS/ICD documents available at:
  http://www.navcen.uscg.gov/index.php?pageName=gpsReferenceInfo/
  http://www.gps.gov/technical/icwg/
Notes: <number>

## Slide 4: Future Performance Standard Updates
Planning a draft update of the SPS PS in 2011
  Addition of L2C signal to current L1 C/A signal
  Same performance values
  Update to be approved before Initial Operational Capability (IOC) declaration for L2C
Planning subsequent draft updates for L5 & L1C signals
  Prior to each subsequent IOC declaration
Developing an updated set of performance metrics
  Include different user applications and terrain environments
<number>

## Slide 5: Nationwide Differential GPS (NDGPS)
Operated/managed by U.S. Coast Guard as a Combined NDGPS
  Includes Maritime + Department of Transportation + Army Corps of Engineers sites
System Specifications
  Corrections broadcast at 285 and 325 kHz using Minimum Shift Keying (MSK) modulation
  Real-time differential GPS corrections provided in Radio Technical Commission for Maritime Services (RTCM) SC-104 format
  No data encryption
  Real-time differential corrections for mobile and static applications
More than 92% of Continental U.S. has single coverage
More than 65% of Continental U.S. has dual coverage
<number>
Notes: <number>

## Slide 6: Nationwide Differential GPS
Expansion of maritime differential GPS (DGPS) network to cover terrestrial United States
Built to international standard adopted in 50+ countries
<number>
Notes: 03/12/08
<number>

## Slide 7: NDGPS Capabilities and Uses
Transportation
  Maritime
    U.S. Coast Guard Aids to Navigation Positioning and maritime navigation
  Traffic congestion
  Baseline reference for railroads
  Used by U.S. Federal Highway Administration
    Roadside management
    Survey, construction, quality, asset management
Other Uses
  Federal-Aid Program
  Law Enforcement
  Resource Management
<number>
  Environmental and Geological Monitoring
  U.S. Army Corp of Engineers Surveying and Dredging operations
Notes: <number>

## Slide 8: National Continuously Operating Reference Stations (CORS)
Enables highly accurate, 3-D positioning
  Centimeter level accuracy via post processing
  Tied to National Spatial Reference System
1,450+ sites operated by 200+ public, private, academic organizations
NOAA’s Online Positioning User Service (OPUS) automatically processes coordinates submitted via the web from around the world
OPUS-RS (Rapid Static) declared operational in 2007
NOAA considering support for real-time networks
<number>
Notes: <number>

## Slide 9: CORS Applications
Primary application is to enable accurate positioning relative to the National Spatial Reference System
Other applications include earth and scientific research
  Monitoring earth tectonic motion
  Sea level change
  Atmospheric studies
  Aerial mapping
<number>
Notes: <number>

## Slide 10: U.S. GPS Augmentation Programs Designed for Aviation
<number>
GBAS
Notes: <number>

## Slide 11: Ground Based Augmentation System (GBAS)
Architecture
  Ground Station/Processing Unit/Power Supply (one shelter on airport property)
  4 Reference Receivers/Antennas
  VHF Data Link Antenna
Specifications
  Supports Category I approach with growth to Category III
  Single facility can provide service up to 23 mile radius
<number>
Notes: <number>

## Slide 12: Ground Based Augmentation System (GBAS)
Aviation Capabilities
Precision approach for ILS Category - I, II, III approaches
Multiple runway coverage at an airport
3D RNP procedures (can be supported by multiple navigation sources)
Continuous Descent Arrivals (CDA)
Navigation for closely spaced parallel runways
Designed for aviation use
<number>
Notes: <number>

## Slide 13: GBAS Category I Implementation
Operational Implementation
  GBAS implementation at Newark
    Straight in procedures developed
    Airspace Simulations in progress for other scenarios
    Flight Inspection 2010 / First Flight TBD
    Continental Airlines taking delivery of GBAS capable 737NG
    ISSUES
      RFI issues on L1 – FAA Spectrum investigating
      NOTAM to address non-availability
  GBAS implementation Houston
    Memphis GBAS will be relocated to Houston
    Houston as an additional airport to establish city pair for Continental
<number>
Notes: <number>

## Slide 14: GBAS Category II/III Acquisition Planning
Drafting/updating required documents according to FAA Acquisition Management System
  Single Competitive Contract Award for Development and Production options
  CAT I/II/III GBAS ground facility
  Low Rate Initial Production (LRIP) beginning around 2015 (IOC)
  10-12 installations per year, up to 90 installations
  20 year life-cycle ~2034
Next Milestones
  Investment Analysis Readiness Decision – September 2011
  Initial Investment Decision – March 2012
  Final Investment Decision – September 2012
<number>
Notes: <number>

## Slide 15: GBAS International Activities
International GBAS Working Group (IGWG)
  Last working group hosted by EUROCONTROL
  June 3-6, 2010 in Brussels, Belgium
  Service providers starting transition from
  research to implementation of GBAS
  Major topics of interest/cooperation
    Coordination of worldwide Ionospheric activities
    Post Implementation activities
    Future applications/CAT II/III CONOPS
GBAS in SESAR (Single European Sky ATM Research)
  SESAR budget includes substantial budgets for GBAS R&D
FAA supporting international ANSP requests for GBAS technical support
  Australia, Brazil, Germany, Spain, Chile, India, China, Colombia
<number>
Notes: <number>

## Slide 16: GBAS Usage
Current airlines GBAS equipped
  Continental, Delta Airlines, Qantas, Air Berlin, TuiFly, Sonair, Air Vanuatu, Emirates
More than 15 countries have active GBAS programs
<number>
Installed
Planned
S-CAT I
Notes: <number>

## Slide 17: Wide Area Augmentation System (WAAS)
Satellite Based Augmentation System (SBAS)
Designed for aviation use, but available and used by many GPS users today
Localizer Performance with Vertical Guidance (LPV)-200 approach is comparable to ILS Category I
<number>
Notes: <number>

## Slide 18: Wide Area Augmentation System (WAAS) Architecture
<number>
38 Reference
Stations
3 Master
Stations
6 Ground
Earth Stations
3 Geostationary
Satellite Links
2 Operational
Control Centers

## Slide 19: WAAS Geo Satellites
<number>
WAAS GEOs (CRE and AMR) Currently Operating
CRW turned OFF in December 2010
  Performance deemed inadequate for WAAS service use
  Total loss of T&C April 2010 resulted in uncontrolled easterly drift
CRW recovery efforts initiated 24 December 2010
  Satellite units undergoing test & evaluation
  Projected possible return to WAAS service in Spring 2011
Potential alternative would utilize former WAAS GEO (POR) to mitigate loss of service in Alaska

## Slide 20: WAAS Availability
<number>

## Slide 21: WAAS Phased Upgrades
<number>
Phase I: IOC (July 2003) Completed
  Provided LNAV/VNAV/Limited LPV Capability
Phase II: Full LPV (FLP) (2003 – 2008) Completed
  Improved LPV availability in CONUS and Alaska
  Expanded WAAS coverage to Mexico and Canada
Phase III: Full LPV-200 Performance (2009 – 2013)
  Software enhancements, hardware upgrades
  Steady state operations and maintenance
  Transition to FAA performed 2nd level engineering support
  Begin GPS L5 transition activities
Phase IV: Dual Frequency (L1,L5) Operations (2013 – 2028)
  Complete GPS L5 transition
  Will significantly improve availability and continuity during severe solar activity
  Provide additional protection against GPS interference
  Will continue to support single frequency users

## Slide 22: Airports with WAAS LPV Approach
As of 18 November 2010
- 2,341 LPVs serving 1231 Airports
1,449 LPVs to non-ILS Runways
892 LPVs to ILS runways
946 LPVs to Non-ILS Airports
plus ~30 Canadian Airports
<number>

## Slide 23: WAAS/SBAS Aviation Benefits
Increased Runway Access
More direct en route flight paths
New precision approach services
Reduced and simplified equipment on board aircraft
Potential elimination of some ground-based navigation aids (NDB, VOR, ILS) can provide a cost saving to air navigation service provider
<number>
Notes: <number>

## Slide 24: Accuracy with Augmentation
<number>

## Slide 25: GPS/WAAS Aviation Performance
<number>
* Use of GPS vertical not authorized for aviation without
augmentation (SBAS or GBAS)
WAAS Performance evaluated based on a total of 1,761 million samples (or 20,389 user days)
 | GPS Standard | GPS Actual | WAAS LPV-200 Standard | WAAS Actual
Horizontal 95% | 36 m | 2.74 m | 16 m | 1.08 m
Vertical 95% | 77 m | *3.89 m | 4 m | 1.26 m

## Slide 26: Precision with Augmentation
<number>
NavCom/Starfire Receiver
  20 cm horizontal accuracy
  30 cm vertical accuracy
Global Satellite Based Augmentation System (GSBAS) Technology developed by NASA’s Jet Propulsion Laboratory

## Slide 27: Summary
GPS Interface Documents are available on the Internet
Plans in work for update to GPS Performance Standard
NDGPS and CORS augmentation systems allow for a range of services free of charge to users throughout the service area
GBAS continues progress toward providing advanced aviation capabilities
  Ultimate goal is to provide Category III precision approach
WAAS upgrades/system improvements occurring in phases
  On schedule for Full LPV-200 Performance in 2013
<number>

## Slide 28: Contact Information
<number>
Jeffrey Auerbach
GNSS Policy Advisor
Office of Space and Advanced Technology
U.S. Department of State
OES/SAT, SA-23, Suite 410
Washington, D.C. 20520
+1.202.663.2388 (office)‏
auerbachjm@state.gov
http://www.state.gov/g/oes/sat/
http://gps.faa.gov/
http://www.pnt.gov/
Notes: 03/12/08
<number>